## Slide 1
Chapter 05 · Methodology
p. ??
Why the objective is a ratio, D / P
Copyright © 2026 Center for Internet of Things Innovation, NTUST. All rights reserved.
版權所有 © 2026 國立臺灣科技大學 物聯網創新中心
The data and material contained in this file is copyrighted.
Please do not use without the author's permission.
本檔案所含資料受著作權保護，未經所有人之同意請勿擅自使用
Every dispatch spends distance D (metres) and earns fulfilment P (line-equivalents). D − P has no physical meaning until you declare what a metre is worth in lines.
Four ways to reconcile them — the first three need a number you cannot measure
min D s.t. P ≥ target
needs a target you cannot fix online
max P s.t. D ≤ budget
needs a budget you cannot fix online
min D − λP
needs an exogenous exchange rate λ
min D / P
needs nothing
M1G / Jiao: α₁ = −40, α₂ = 1, α₃ = 1000 — tuned by preliminary experiments
this study
λ is not a preference parameter. It is a system state that drifts with fleet size and station saturation — fixing it by hand delegates modelling to tuning.
The KPIs we report are ratios — energy per order, metres per line. The objective should be the ratio we report.
Optimising a weighted sum while reporting a ratio optimises something other than what is measured.
Why the ratio is the natural quantity here
No free parameter
The exchange rate becomes an output of the model,
not an input from the modeller
Scale-free
D and P both grow with the horizon; their ratio
does not — 2 h and 8 h stay comparable
Matches what we measure
Fixed-λ sweep optimum 14–24 lands on the measured
marginal price 13.7–18 → a physical quantity
Denominator is line-equivalents, not orders — otherwise a 1-line and a 10-line order count the same; order credit converts back through μ = λ (L / N). Known weakness: a ratio degenerates as P → 0, so "do nothing" is formally optimal — this is exactly what the upper-bound step exists to correct.