## Slide 1
Chapter 05 · Methodology
Baseline: M1 — Online Joint OA–PS–TA Optimization Model
Copyright © 2026 Center for Internet of Things Innovation, NTUST. All rights reserved.
版權所有 © 2026 國立臺灣科技大學 物聯網創新中心
第 24 頁
Sets and Parameters
Pending orders
Workstations with free capacity
SKUs in Warehouse
All pods; Idle pods; Pods already assigned to Workstations
All robots; Idle robots; Busy robots
Orders demanding SKU i; Pods holding SKU i
Units of SKU i in Order o; Units of SKU i on Pod p
Free capacity of Workstation;Counted in ORDERS; Pod-Station and Robot-Pod distance
Objective (14)
Constraints (2) – (13)
(2)
one order to at most one workstation
(3)
an assignable order is not necessarily assigned
(4)
assigned orders equal capacity minus unused capacity
(5)
demand for SKU i at w cannot exceed what the pods at w supply
(6)
a pod goes to at most one workstation
(7)
inherit pods already assigned to w
(8)
dispatching a pod requires a robot
(9)
a pod is transported by at most one robot
(10)
a robot transports at most one pod
(11)
a busy robot continues its current transport task
(12)
supply requires the order assigned AND the pod assigned
(13)
a newly assigned pod must supply at least one assigned order
The data and material contained in this file is copyrighted.
Please do not use without the author’s permission.
本檔案所含資料受版權保護，未經所有人之同意請勿擅自使用
CITI
Center for IoT Innovation
Order o COULD be assigned to Workstation — not slot-limited
Order o IS assigned to Workstation — consumes a slot
Pod p is assigned to Workstation w
Robot r transports Pod p — task allocation is inside the model
Auxiliary: pod p supplies order o at w
unused capacity of workstation w
Decision Variables
Jiao, G., Huang, M., Song, Y., Li, H., & Wang, X. (2026). Online joint optimization of order picking process in robotic mobile fulfillment systems. Omega, 138, 103374.
(16)
(15)
(14)
Trigger OJOOPT decision standard - Different from delta above

## Slide 2
Chapter 05 · Methodology
Proposed Exact Model: M4 — Online Joint OA–PS–TA Order Splitting Optimization Model
The data and material contained in this file is copyrighted.
Please do not use without the author’s permission.
本檔案所含資料受版權保護，未經所有人之同意請勿擅自使用
CITI
Center for IoT Innovation
Copyright © 2026 Center for Internet of Things Innovation, NTUST. All rights reserved.
版權所有 © 2026 國立臺灣科技大學 物聯網創新中心
第 25 頁
The Decision Atom
one order
units of SKU i of order o, drawn from pod p, at station w
Splitting is what this variable permits — not a feature added on top.
Constraints That Carry a Modelling Choice
V1
draw only what that pod carries, and only if it is sent
V3
a line counts only when it is drawn in full
B1
what is executed is a subset of what is valued
B3
a station holds a fixed number of orders at a time
Pod and robot constraints — one pod per station, one robot per pod, inheritance of assignments already committed — are the physical rules of the floor and are carried over unchanged.
Why a Ratio, and How It Is Solved
D distance walked
V value delivered
metres walked per unit of value delivered. A weighted sum would first need an answer to “how many metres is an order worth”. A ratio does not.
a solver minimises linear expressions, not divisions — so guess the rate λ and ask whether any plan beats it
F > 0 raise
F < 0 lower
1 guess a rate λ
2 solve min D − λV
3 read the rate it achieved
4 adopt it, repeat
F is decreasing, so the root is unique; the update is Newton's method on F. [Dinkelbach 1967]
What the Two Coefficients Mean
β seen → done
valued
bound
the share of what the model can see that it can execute now
a bound line earns the full price; a line only seen earns λβ
ρ which pod you drain
− ρ
being picked now
+ ρ
dispatched now
0
still en route
taking a unit from a pod about to leave saves a future trip; taking one from a pod fetched now costs an extra trip. ρ prices which pod is drained, not how far it travelled.

## Slide 3
Chapter 05 · Methodology
Solving M4 — Dinkelbach Transform and Self-Calibrated Prices
The data and material contained in this file is copyrighted.
Please do not use without the author’s permission.
本檔案所含資料受版權保護，未經所有人之同意請勿擅自使用
CITI
Center for IoT Innovation
Copyright © 2026 Center for Internet of Things Innovation, NTUST. All rights reserved.
版權所有 © 2026 國立臺灣科技大學 物聯網創新中心
第 26 頁
Why the Ratio Cannot Be Solved Directly
A MILP solver minimises a LINEAR expression. Division is not linear, so this cannot be handed to the solver as written.
Read the transform as a budget: at the guessed rate lambda, V units of value are worth lambda-V metres, and D is what the plan actually spends. Under budget means the plan beat the rate.
The Test, and the Loop
some plan beats the rate → lower lambda
no plan reaches it → raise lambda
the best plan exactly breaks even → lambda is optimal
F is decreasing in lambda, so the root is unique: the ratio problem becomes a one-dimensional root search.
1. Guess a rate start from the running measured value
2. Solve the linear subproblem min D − lambda-V — this the solver can do
3. Read the rate that plan achieved D* / V*
4. Adopt it and repeat until the objective is within tolerance
this is Newton's method on F, hence the quadratic convergence
Measured: 96 % of decisions converge within a single update (0 updates 444, 1 update 449, of 929). Stop at |objective| <= 0.5 m or 5 iterations. The theorem needs V > 0; doing nothing gives V = 0, so that case doubles lambda instead, at most 6 times.
Where the Prices Come From
Travel distance is the only measured quantity. Each price is that distance divided by a different counter of work done.
derived from
unit
measured median
distance / closed lines
metres per line
8.06
lambda x lines per order
metres per order
12.22
distance / units picked
metres per unit
3.70
0.001 x lambda
metres per unit
0.008
bound lines / valued lines
dimensionless
0.188
No price is set by the modeller. The hand-set numbers are the warm-up seeds, used for the first 50 closed lines only, and the epsilon scale — a tie-break three orders of magnitude below lambda.
Two Invariants the Design Rests On
1. The price ratios are fixed by the instance, not chosen.
Dinkelbach only works if V keeps its SHAPE while lambda searches, so every price scales with lambda together and only the level moves. mu / lambda is lines per order; rho / lambda is the reciprocal of units per line — both properties of the instance.
2. beta is bounded on both sides, and the measured value sits inside.
beta
what the model does
result
0
credits a pod only for the line it can bind now
pile-on 6.04 → 4.13, energy +24.5 %
0.19
credits unusable coverage at the measured rate
the canonical setting
≥ 0.5
execution earns nothing at the margin
the run stops producing orders
beta is conditioned on how many pods are already committed: slot capacity pins the binding layer near one line per decision while the valuation layer grows with committed supply, so a further pod is scored for coverage the binding layer cannot take.