## Slide 1
Chapter 05 · Methodology
Baseline: M1 — Online Joint OA–PS–TA Optimization Model
Copyright © 2026 Center for Internet of Things Innovation, NTUST. All rights reserved.
版權所有 © 2026 國立臺灣科技大學 物聯網創新中心
第 24 頁
Sets and Parameters
Pending orders
Workstations with free capacity
SKUs in Warehouse
All pods; Idle pods; Pods already assigned to Workstations
All robots; Idle robots; Busy robots
Orders demanding SKU i; Pods holding SKU i
Units of SKU i in Order o; Units of SKU i on Pod p
Free capacity of Workstation;Counted in ORDERS; Pod-Station and Robot-Pod distance
Objective (14)
Constraints (2) – (13)
(2)
one order to at most one workstation
(3)
an assignable order is not necessarily assigned
(4)
assigned orders equal capacity minus unused capacity
(5)
demand for SKU i at w cannot exceed what the pods at w supply
(6)
a pod goes to at most one workstation
(7)
inherit pods already assigned to w
(8)
dispatching a pod requires a robot
(9)
a pod is transported by at most one robot
(10)
a robot transports at most one pod
(11)
a busy robot continues its current transport task
(12)
supply requires the order assigned AND the pod assigned
(13)
a newly assigned pod must supply at least one assigned order
The data and material contained in this file is copyrighted.
Please do not use without the author’s permission.
本檔案所含資料受版權保護，未經所有人之同意請勿擅自使用
CITI
Center for IoT Innovation
Order o COULD be assigned to Workstation — not slot-limited
Order o IS assigned to Workstation — consumes a slot
Pod p is assigned to Workstation w
Robot r transports Pod p — task allocation is inside the model
Auxiliary: pod p supplies order o at w
unused capacity of workstation w
Decision Variables
Jiao, G., Huang, M., Song, Y., Li, H., & Wang, X. (2026). Online joint optimization of order picking process in robotic mobile fulfillment systems. Omega, 138, 103374.
(16)
(15)
(14)
Trigger OJOOPT decision standard - Different from delta above

## Slide 2
Chapter 05 · Methodology
Proposed Exact Model: M4 — Online Joint OA–PS–TA Order Splitting Optimization Model
The data and material contained in this file is copyrighted.
Please do not use without the author’s permission.
本檔案所含資料受版權保護，未經所有人之同意請勿擅自使用
CITI
Center for IoT Innovation
Copyright © 2026 Center for Internet of Things Innovation, NTUST. All rights reserved.
版權所有 © 2026 國立臺灣科技大學 物聯網創新中心
第 25 頁